## Slide 1: Mobility @ w-iLab.t Zwijnaarde
Pieter Becue
Vincent Sercu

## Slide 2: Mobility @ w-iLab.t

## Slide 3: Mobility Extension (Zwijnaarde)
allow experiments with mobile nodes
based on vacuum cleaning robot
  extended with:
    iMinds Robotcontrol
      In-house designed circuit board (Power control)
      radio for remote control (ez430 – 868MHz)
    Embedded PC
      Powered by external battery pack
      Webcam
      Wireless interfaces :
        802.11a/b/g/n
        Bluetooth
        iMinds Rmoni sensor node (802.15.4)

## Slide 4: iMinds Robotcontrol
  In-house designed
  Power distribution
    Charge battery pack through Roomba dock (modified)
    Power On/Off embedded PC
  Toggle robot “eyes” (leds)
  Expansion pins
    Radio for remote control (eZ430 – 868 MHz )

## Slide 5: Controlled & Reproducible
  High accuracy positioning algorithm
  Full control over experiment node (PC + Sensor)
  Fully integrated into testbed (OMF)
  User can fully control robot behavior
  Mobile node measurements stored through OML

## Slide 6: User tools
Network PTZ camera’s
  Visual feedback
Easy path generation
  Auto-detection of collisions
    Between robots
    With obstacles
    Time-sensitive
  Loading/saving coordinate files
     Used in OMF Experiment Description
  With simulator

## Slide 7: OMF Integration
New OEDL commands
  Start robot path
    Based on coordinate files
    Auto dock/undock (from safe zone)
  Toggle robot “eyes”
  Power embedded PC
Custom events
  Based on robot position
    Known inside ED
  Based on measurement data
  Execute any OEDL command

## Slide 8: Demo
User tools
OMF-integration

## Slide 9: The w-iLab.t testbed
details:
www.crew-project.eu/portal/w-ilabt
Questions?
Questions?
http://ilabt.iminds.be
pieter.becue@intec.ugent.be
bart.jooris@intec.ugent.be
vincent.sercu@intec.ugent.be
www.ibcn.intec.ugent.be – www.iminds.be